## Slide 1: Real-Time 3D Semantic Mapping with Multimodal Data for Autonomous Robotic Navigation
Student: Nicolò Giovanni Agostara ID: 897237 | Supervisor: Prof. Paolo Napoletano | External-Supervisor: Prof. Volker Krueger

## Slide 2: Motivation and background
Combining RGB and depth data improves object detection and localization accuracy
3D semantic mapping enables robots to identify, reach and interact with objects in complex environments.
Real Time performance is critical for practical robotic applications

## Slide 3: Objective
The objective is to design, deploy and test a 3D semantic mapping system that incrementally builds a 3D map with objects identities and volumes in real world scenarios.
Noise Reduction
Implements techniques to handle depth noise.
Multimodal Data Fusion
Combines visual and spatial data for object representation.
Object Re-identification
Uses KD-Trees to avoid redundancy and re-identify objects.

## Slide 4: Heron Robot
Powerfull Computational Resources
RGB-D Camera for 3D perception
Robotic Operative System 1 (ROS1)
High precision positioning system
Pre-built autonomous navigation stack

## Slide 5: System architecure Overview

## Slide 6: Instance Segmentation and Tracking
YOLOv8
Performs object instance segmentation with high detection accuracy, ensuring real time efficiency.
ByteTrack
Performs 2D Multi-Object Tracking (MOT) with unique IDs for each object, offering high speed and robustness against occlusions.

## Slide 7: Object Projection
1
Apply Mask to Depth Image
Extracts object-specific depth information by applying segmentation mask
Project to Camera Coordinates
Transforms masked depth data into a 3D point cloud in the camera’s coordinate frame
2
Transform to World Coordinates
Query ROS for the roto-translation matrix at time t to transform the object’s 3D points in the world frame. Ensuring spatial consistency between objects
3

## Slide 8: Object Projection
1
Apply Mask to Depth Image
Extracts object-specific depth information by applying segmentation mask
Project to Camera Coordinates
Transforms masked depth data into a 3D point cloud in the camera’s coordinate frame
2
Transform to World Coordinates
Query ROS for the roto-translation matrix at time t to transform the object’s 3D points in the world frame. Ensuring spatial consistency between objects
3

## Slide 9: Object Projection
1
Apply Mask to Depth Image
Extracts object-specific depth information by applying segmentation mask
Project to Camera Coordinates
Transforms masked depth data into a 3D point cloud in the camera’s coordinate frame
2
Transform to World Coordinates
Query ROS for the roto-translation matrix at time t to transform the object’s 3D points in the world frame. Ensuring spatial consistency between objects
3

## Slide 10: Point Cloud Preprocessing
1
Voxel Down Sampling
Voxel down sampling reduces point cloud density by retaining only one point per voxel, optimizing memory and enabling faster processing without losing essential structural details.
Noise Removal
Statistical outlier removal filters isolated points, while radius outlier removal targets sparse regions, improving point cloud quality.
2
Projected Point Cloud

## Slide 11: Point Cloud Preprocessing
Down-sampled Point Cloud
1
Voxel Down Sampling
Voxel down sampling reduces point cloud density by retaining only one point per voxel, optimizing memory and enabling faster processing without losing essential structural details.
Noise Removal
Statistical outlier removal filters isolated points, while radius outlier removal targets sparse regions, improving point cloud quality.
2

## Slide 12: Point Cloud Preprocessing
Cleaned Point Cloud
1
Voxel Down Sampling
Voxel down sampling reduces point cloud density by retaining only one point per voxel, optimizing memory and enabling faster processing without losing essential structural details.
Noise Removal
Statistical outlier removal filters isolated points, while radius outlier removal targets sparse regions, improving point cloud quality.
2

## Slide 13: 3D Object Re-Identification
In 2D tracking, objects exiting and re-entering the field of view are assigned new IDs but we need to maintain a consistent identity for each object to ensure accurate tracking over time and avoid adding redundant objects.
New Detection
World Model
Close Objects
Merge Objects
Add new object
Overlap?
Query
Not Found
Found
No
Yes

## Slide 14: World Model – KD-Trees
Efficient Spatial Organization
Organizes object centroids hierarchically, based on their coordinates in space.
Rapid Spatial Queries
Enables fast nearest-neighbour searches, essential for locating nearby objects.

## Slide 15: Point Cloud Overlap
Stored object
New detection
Compute Intersection
Identify intersecting regions between the grids, preparing for similarity calculation.
Create 3D Occupancy Grid
Create for each point cloud a 3D occupancy grid. This standardizes the point cloud resolution and enables direct comparison between different point clouds
Compute Dice Coefficient
Calculate the Dice Coefficient to quantify overlap. If it exceeds a threshold, the clouds are considered to represent the same object.

## Slide 16
Point Cloud Overlap
Stored object
New detection
Compute Intersection
Identify intersecting regions between the grids, preparing for similarity calculation.
Create 3D Occupancy Grid
Create for each point cloud a 3D occupancy grid. This standardizes the point cloud resolution and enables direct comparison between different point clouds
Compute Dice Coefficient
Calculate the Dice Coefficient to quantify overlap. If it exceeds a threshold, the clouds are considered to represent the same object.

## Slide 17
Point Cloud Overlap
Difference
Intersection
Compute Intersection
Identify intersecting regions between the grids, preparing for similarity calculation.
Create 3D Occupancy Grid
Create for each point cloud a 3D occupancy grid. This standardizes the point cloud resolution and enables direct comparison between different point clouds
Compute Dice Coefficient
Calculate the Dice Coefficient to quantify overlap. If it exceeds a threshold, the clouds are considered to represent the same object.

## Slide 18: Point Cloud Overlap
Compute Intersection
Identify intersecting regions between the grids, preparing for similarity calculation.
Create 3D Occupancy Grid
Create for each point cloud a 3D occupancy grid. This standardizes the point cloud resolution and enables direct comparison between different point clouds
Compute Dice Coefficient
Calculate the Dice Coefficient to quantify overlap. If it exceeds a threshold, the clouds are considered to represent the same object.

## Slide 19: Data Collection and Annotation
Collection Method
Manual Navigation of Heron Robot in 7 different Environments with RTAB-MAP used for environment reconstruction
Dataset Overview
101 ground truth objects across 13 categories
Chart: 
| Chair | TV | Dining Table | Keyboard | Mouse | Laptop | Person | Backpack | Handbag | Bottle | Cup | Couch | Scissors
Count | 29 | 24 | 10 | 7 | 6 | 5 | 4 | 3 | 3 | 3 | 3 | 2 | 2
Data Annotation
The final reconstructed environment undergo labelling and bounding boxes annotation with LabelCloud

## Slide 20: Evaluation Method
Compute TP, FP, FN
From these sets compute True Positives (TP), False Positives (FP) and False Negatives (FN) for each class
Match Ground Truth and Predicted Objects
Using a minimum overlap threshold, we extract sets of matching pairs, missed ground truths and phantom predictions
Metrics
Mean Average Precision (mAP)
Macro averaged Precision
Macro Averaged Recall
Macro Averaged F1-Score
Frames Per Second (FPS)
Matching pairs
Phantom Prediction
Missed Ground Truth

## Slide 21: Results – Time Analysis
Average object number for each frame | FPS
1 | 22.73
2 | 11.36
3 | 7.58
4 | 5.68
5 | 4.55
The /objects topic uses a queue size of 5 to retain only the most recent detections, preventing backlog buildup.
System Performance Evaluation
Execution times measured across Detection, Mapping and World nodes.
Asynchronous Processing
Each node runs on separate threads, enabling parallel processing.
FPS Bottleneck:
Since Detection and Mapping nodes exceed 30FPS, only the World node affects the overall frame rate.

## Slide 22: Results – Performance Metrics
Chart: Overlap Threshold
| 0,05 | 0,1 | 0,15 | 0,2 | 0,25 | 0,3 | 0,35 | 0,4 | 0,45 | 0,5 | 0,55 | 0,6 | 0,65 | 0,7 | 0,75 | 0,8 | 0,85 | 0,9 | 0,95 | 1.00
mAP | 0.81 | 0.803 | 0.803 | 0.803 | 0.803 | 0.803 | 0.799 | 0.799 | 0.77 | 0.758 | 0.744 | 0.682 | 0.581 | 0.405 | 0.316 | 0.079 | 0.03 | 0 | 0 | 0
Precision | 0.77 | 0.76 | 0.76 | 0.76 | 0.76 | 0.76 | 0.75 | 0.75 | 0.72 | 0.7 | 0.68 | 0.6 | 0.59 | 0.49 | 0.41 | 0.26 | 0.16 | 0.01 | 0 | 0
Recall | 0.92 | 0.91 | 0.91 | 0.91 | 0.91 | 0.91 | 0.9 | 0.9 | 0.86 | 0.83 | 0.8 | 0.71 | 0.69 | 0.59 | 0.49 | 0.31 | 0.19 | 0.02 | 0 | 0
F1-Score | 0.84 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.82 | 0.82 | 0.78 | 0.76 | 0.74 | 0.65 | 0.64 | 0.53 | 0.45 | 0.28 | 0.17 | 0.01 | 0 | 0
Metrics evaluated at different overlap thresholds to assess performance across varying levels of spatial alignment.
High results with low thresholds indicates good detection and localization performances
Performance decreases as overlap thresholds increase, indicating challenges in object volume reconstruction.
2
3
1

## Slide 23: Conclusions
Key Contributions
The system enables 3D semantic mapping leveraging multimodal data, addressing object detection, re-identification, and noise removal challenges.
Future Directions
Enhance performance in dynamic environments, improve system efficiency, and experiment with different depth sensors.
Achievements
The system achieves 80% mAP at a 0.4 minimum overlap threshold, maintaining an average processing speed of 11 FPS in the tested environments.

## Slide 24
Thank You!